## Slide 1: Technical overview LoRaWAN network Professor: Dr.Mehdi Rasti Lecturer: Jaber Babaki Amirkabir University of Technology Spring 2021

## Slide 2: HELLO!
I AM JABER BABAKI
You can find me at:
Email: jaber.babaki@gmail.com
GitHub: https://github.com/JaberBabaki
Linkedin: https://www.linkedin.com/in/jaber-babaki-9b5474102/
Telegram: @jaberALU

## Slide 3: Agenda
3- LoRaWAN Network
Protocol stack
LoRaWAN architrcture
End to End communication
1- Big concept
IoT definition
IoT architecture
Technical research challenges
2- Communication technologies
Defination Communication technologies
Long Range criteria
Compare Long Rage technologies
4- CSS modulation
Chrip signal
Spread factor
Symbol rate
5- RF Factor
Link budget
Receiving sensitivity
SNR
Maximum daily packets on LoRaWAN
6- ALOHA
Defination ALOHA
Analysis ALOHA
7- LoRaWAN performance
Maximum throughput
Maximum Number

## Slide 4: BIG CONCEPT
Let’s start with big concept about "Internet of Thing" and "Long Range Wide Area Network"
1

## Slide 5: Introduction
The Internet of Things (IoT) is an extension of the Internet in which large numbers of “things”, including sensors, actuators and processors, in addition to human users, are networked and able to provide high resolution data on their environment and exercise a degree of control over it[1].
The principal advantage of IoT consists of its ability to enable communication between an infinite amount of machines incorporated into a large-scale wireless network[1].
These automated devices and sensors together produce and transmit information in real-time, which is useless in the case of incorrect or insufficient filtering and data processing[1].

## Slide 6: Introduction
IoT Edge Device
IoT Sensor
Bulk Device Provisioning
etc.,
Cloud Server
IoT Gateway/
Framework
Stream Processing
Things
Insights
Action
User
Management
User
Interface
Machine
Learning
Reporting
Tools
Data Transformation
Figure 1: Abstract architectures[2].

## Slide 7: Introduction
Many of these are technical, including interoperability and scalability
How to invest in the IoT is a challenge for business
Major social, legal and ethical challenges, including security and privacy
As the future IoT will be a multi-national, multi-industry, multi-technology infrastructure
[1] Peter J. Ryan 1 and Richard B. Watson, “Research Challenges for the Internet of Things: What Role Can OR Play?”, systems journal, 14 March 2017 .

## Slide 8: The main IoT technical research challenges
Design
Architecture
Interoperability
Scalability
Mobility
Security and Privacy
Scientific/Engineering
Energy efficiency/ Power
Reliability /Robustness
Management/ Operation
Software
Development
Availability
Data management
Cloud computing
[1] Peter J. Ryan 1 and Richard B. Watson, “Research Challenges for the Internet of Things: What Role Can OR Play?”, systems journal, 14 March 2017 .

## Slide 9: Communication technologies
2

## Slide 10: Communication and transport technologies
An essential requirement for implementing a large and cooperating network of devices is the ability to have a flexible, inexpensive and adaptive connectivity layer.
For these reasons, during the years, several wireless connectivity standards have emerged, ranging from very short-range, low power connections to long-range connectivity solutions based on cellular technologies.
While short-range protocols can be successfully used for a number of applications (e.g., smart homes, wearable, etc.), for many other applications larger coverage radii become mandatory.
[3] LPWAN white paper, Leverege LLC, 2020 | www.leverege.com

## Slide 11: Communication and transport technologies
We expect that in 2024 more than the 40% of the wide area M2M connections will be LPWAN. That is why several companies are developing different protocols to implement the LPWAN technology.
[3] LPWAN white paper, Leverege LLC, 2020 | www.leverege.com

## Slide 12: Communication and transport technologies
To compare the protocols we keep in mind some of the most important characteristics of the LPWAN and some others important features like:
Range: We all know that the range of any wireless technology can vary based on what is in the way of the signal. A dense urban setting, with walls, buildings, reflections, lots of other people and traffic, means much shorter range than a rural one. And a at, unobstructed rural setting will behave better than a hilly one.
Band and spectrum: As we have explained there are protocols that use the free ISM band and others that use licensed spectrum. We can see also differences into the spectrum use, there are some protocols that use Ultra Narrow Band, some are Narrow Band, and some others like LoRa uses Spread Spectrum (Chirp Spread Spectrum).
[3] LPWAN white paper, Leverege LLC, 2020 | www.leverege.com

## Slide 13: Communication and transport technologies
Data Rate: This is another highly variable parameter, it can depend on the distance to the receptor, the obstructions...
Over-the-air updates: This may sound like a random characteristic, but it can be important depending on the application and the deployment of the end-devices. When the number of end-devices is hight or the devices are placed on a remote place, we will get greats advantages of this feature.
Handover: IoT has an extensive application fields, we will find applications where the end-devices will be static units, in other cases they will be mobile (vehicles in urban or rural areas, for farm implementations for example). So it is natural to wonder whether a protocol that can handle the hand-off a device as it moves between hubs, this matters only to the extent that a "session" of some sort is being maintained.
[3] LPWAN white paper, Leverege LLC, 2020 | www.leverege.com

## Slide 14: Communication and transport technologies
 | LoRa | SIGFOX | Telensa | ingenu
Range [km] | 3-8 urban 15-20 suburban | 3-10 urban 30-50 suburban | Up to 8 | 4
Band | Sub-GHz | Sub-GHz | Sub-GHz | 2.4 GHz
Modulation | Spread Spectrum | Ultra-Narrow Band | Ultra-Narrow Band | Spread Spectrum
Data Rate [kbps] | 0.3-22 | 0.1-0.6 | low | 20
OTA upgrades | Yes | No | Yes | Yes
Handover | No | Yes | Yes | Yes
Table 1: A Comparison of LPWAN Technologies [3].

## Slide 15: LoRaWAN Network
3

## Slide 16: LoRaWAN network
The LoRaWAN network is formed by two core components: LoRa and LoRaWAN, each of which refers to a layer in the protocol stack. LoRa is a physical layer modulation developed by Semtech. LoRaWAN is implemented on top of the LoRa and includes data link and network layers [4].
-----
AS 430[MHz]
US 915 [MHz]
EU 433 [MHz]
EU 868 [MHz]
Regional ISM band
LoRa Modulation
Class A
Class B
Class C
MAC options
LoRa MAC
Application
PHY layer (LoRa)
MAC layer (LoRaWAN)
Application layer
Figure 2: protocol stack.

## Slide 17: LoRaWAN network
As seen in this figure, the nodes send data to the platform through the gateways. Note that the nodes are not assigned to a specific gateway. Rather, all the gateways in the transmission range of a node receive its data and send it to the platform.
4G/Ethernet/WiFi
G1
G2
G3
Network Server
Application Server
Figure 3: LoRaWAN architecture.

## Slide 18: LoRaWAN network
Network Server
Node
Processor
The gateways are connected to the network server via standard IP connections and act as a transparent bridge, simply converting RF packets to IP packets and vice versa.
PHY
SPI
HAL
LoRaWAN Master
Customer Application
BackhaulIP Stack
LoRaWAN Master
Customer Server
Gateway host
PHY
SPI
HAL
Packet Forward
BackhaulIP Stack
Encrypted
Encrypted
LoRa FSK
Ethernet, 4G, WiFi
Figure 4: End-to-End communication[5].

## Slide 19: CSS as a modulation for Long Range
4

## Slide 20: Technical overview CSS as a modulation for Long Range Communication
Long range low power is a family of technologies promising to connect thousands of sensors to the future internet of things. Within this family of possible technology choices, two different branches have emerged
Spread wideband communication
Narrowband communication
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 21: Technical overview CSS as a modulation for Long Range Communication
Frequency
Power
Noise
Narrowband
Spread spectrum
Band of signals occupy a narrow/wide range of frequencies
Power density is high/very low(max power SigFox and LoRa equal 20dBm).
Frequency-hopping spread spectrum (FHSS)
Direct-sequence spread spectrum (DSSS)
Time-hopping spread spectrum (THSS)
Chirp spread spectrum (CSS)
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 22: Technical overview CSS as a modulation for Long Range Communication
Channel Encoder
Input Message
Modulator
Spreading Generator
System
T
F
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 23: Technical overview CSS as a modulation for Long Range Communication
fc
t
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 24: Technical overview CSS as a modulation for Long Range Communication
fc
t
The spreading factor, SF , is the number of bits encoded in each chirp duration.
1
f0
f1
f2
f3
f4
f
f
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 25: Technical overview CSS as a modulation for Long Range Communication
t
t
t
f
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.

## Slide 26: Factors determine RF range
5

## Slide 27: Decibel
A unit of measurement is a definite magnitude of a quantity, defined and adopted by convention or by law, that is used as a standard for measurement of the same kind of quantity.
The decibel (symbol: dB) is a relative unit of measurement corresponding to one tenth of a bel (B). It is used to express the ratio of one value of a power or root-power quantity to another, on a logarithmic scale.
If a person is listening to a radio with a sound power of 10 watts, the volume will not be doubled when it increases the output power to 20 watts.

## Slide 28: Decibel
What if we want to measure an absolute power with dB? We have to define a reference.
The new m in dBm refers to the fact that the reference is one mW, and therefore a dBm measurement is a measurement of absolute power with reference to 1 mW.
The reference point that relates the logarithmic dB scale to the linear watt scale may be for example this:
To convert power in mW to dBm:
To convert power in dBm to mW:
[11] WIRELESS NETWORKING IN THE DEVELOPING WORLD, http://wndw.net

## Slide 29: Decibel
Example: mW to dBm, Radio signal power: 100mW
Example: dBm to mW, Radio signal power: 17dBm
You can now imagine situations in which:
[11] WIRELESS NETWORKING IN THE DEVELOPING WORLD, http://wndw.net

## Slide 30: What factors determine RF range and performance?
Link budget : The link budget is the difference between the strength of the transmitted signal and the minimum required signal at the receiver
Transmitter
Receiver
[7] LoRa™ Modulation Basics, SEMTECH

## Slide 31: What factors determine RF range and performance?
Tx radio
cable
ANT
Rx radio
cable
ANT
Path loss
Figure 5: Example link budget calculation [8].

## Slide 32: What factors determine RF range and performance?
Receiving sensitivity: refers to the smallest modulated signal that can be demodulated at the receiving end.
Thermal noise for a 1 Hz bandwidth
Noise figure
Tx power = 14 dBm
BW = 125KHz = 10log10(125000) = 51
NF = 6 dBm
SNR = -20 dBm(for SF=12)
Rx sensitivity = - 174 + 51 + 6 - 20 = -137 dBm
Link budget = -137dB - 14dB = -151dB
Frequency
Power
Noise
LoRa
SNR is key measure in wireless network.
In LoRa network SNR include Noise, SF, BW, TP, CR, Interference
[7] LoRa™ Modulation Basics, SEMTECH

## Slide 33: What factors determine RF range and performance?
Receiving sensitivity: refers to the smallest modulated signal that can be demodulated at the receiving end.
Thermal noise for a 1 Hz bandwidth
Noise figure
[7] LoRa™ Modulation Basics, SEMTECH

## Slide 34: What factors determine RF range and performance?
Signal-to-Noise Ratio (SNR) : is the ratio between the received power signal and the noise floor power level.
Figure 6: Signal-to-Noise Ratio (SNR) [8].

## Slide 35: What factors determine RF range and performance?
:
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.
Typical values ​​of SNR of LoRa are: -20dB and +10dB.
LoRa can demodulate signals below -7.5dB ~ -20dB below the floor noise.

## Slide 36: What factors determine RF range and performance?
:
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.
Typical values ​​of SNR of LoRa are: -20dB and +10dB.
LoRa can demodulate signals below -7.5dB ~ -20dB below the floor noise.

## Slide 37: What factors determine RF range and performance?
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.
𝑃𝑎𝑡ℎ 𝑙𝑜𝑠𝑠 (PL): Path loss (or path attenuation) delineates a decline in power density of any given electromagnetic wave as it propagates through space.
Path loss models are developed using a combination of numerical methods and empirical approximations of measured data collected in channel sounding experiments.
In general, propagation path loss increases with frequency as well as distance:

## Slide 38: What factors determine RF range and performance?
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.

## Slide 39: What factors determine RF range and performance?
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.

## Slide 40: Maximum daily packets on LoRaWAN
Duration of the packet transmission
 | Description
SF | Spreading Factor
PL | Payload Length
CRC | The use of the Cyclic Redundancy Check (CRC, 1 when enabled 0 when not)
IH | The use of explicit header or not (IH, 1 when enabled 0 when not)
CR | Coding Rate
DE | The Low Data Rate Optimization (DE, 1 when used 0 when not).
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016

## Slide 41: Maximum daily packets on LoRaWAN
The time that the LoRa Mote has to wait before send the next packet is called Toff
So we can calculate the maximum daily packets
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016

## Slide 42: Maximum daily packets on LoRaWAN
 | 16B | 32B | 51B
7 | 60ms | 90ms | 110ms
8 |  |  | 
9 |  |  | 
10 |  |  | 
11 |  |  | 
12 | 161ms | 213ms | 276ms
 | 16B | 32B | 51B
7 | 13061 | 9657 | 7394
8 |  |  | 
9 |  |  | 
10 |  |  | 
11 |  |  | 
12 | 540 | 408 | 316
we can calculate theoretical Ton-the-air and maximum number of daily packets with variable payload, 8 symbols of preamble, CRC activated with a value of 4/5, Implicit Header deactivated, bandwidth of 125 kHz and Low Data Rate optimization activated for high spreading factors (SF11 and SF12).
Table 2: Theoretical Ton-the-air and maximum number of daily packets [10].

## Slide 43: What factors determine RF range and performance?
SF | 125 (kHz) |  |  | 250 (kHz) |  |  | 500 (kHz) |  |  | SNR (dBm) | Range (Km)
 | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) |  | 
7 | 5.4 | -124 | 56 | 110 | -122 | 20 | 219 | -116 | 10 | -7.5 | 2
8 |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  | 
12 | 0.29 | -137 | 1483 | 0.5 | -135 | 495 | 0.98 | -129 | 247 | -20 | 15
Code rate: 4/5 Payload:10 byte
انجام شبیه سازی با پایتون و پر کردن جدول و کشیدن نمدار بر حسب سایز پکت ارسالی

## Slide 44: ALOHA protocol
6

## Slide 45: ALOHA protocol
Channel Encoder
Input Message
Modulator
Spreading Generator
System
T
F
Channel
Designated frequency
Output signal
Designated frequency
Output signal
Channel
Output signal
Channel
.
.
Designated frequency
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016

## Slide 46: ALOHA protocol
TDMA creates channels by assigning users nonoverlapping time slots. In a system with N users, each user can thus use the total bandwidth W, but only a fraction 1/N of the time
1
2
3
4
T
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 47: ALOHA protocol
Node transmits as soon as it has a frame.
If a collision is detected, it waits for a random time interval and then retransmits.
1
2
3
4
T

## Slide 48: ALOHA protocol
Node transmits as soon as it has a frame.
If a collision is detected, it waits for a random time interval and then retransmits.
Channel
PHY
MAC
New packets
Old packets
packets generation rate per end-devices per time
packets rate send per end-devices per time on channel
Collision?
Average packets generation rate per end-devices per time
Average packets send per end-devices per time on channel
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016

## Slide 49: ALOHA protocol implemented on LoRaWAN

## Slide 50: ALOHA protocol

## Slide 51: Slotted-ALOHA protocol
1
2
3
4

## Slide 52: Slotted-ALOHA

## Slide 53: ALOHA protocol implemented on LoRaWAN
7

## Slide 54: ALOHA protocol implemented on LoRaWAN
λ represents all the packets sent to the network by all the LoRa devices in the same coverage area, so we can rewrite λ as:
Each packet sent by one LoRa device, will select randomly one channel from the 8 available, so the total throughput sent by one LoRa devices per channel will be:
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016

## Slide 55: Maximum throughput per end-device and per channel
 | Max. daily packets per end-device [packets/day] | Max. λi per end-device [packets/sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 0,037
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0,001
Considering packets of 16B payload, a bandwidth of 125 kHz and two available sub-bands on LoRaWAN (Band0 from 868.1 MHz to 868.5 MHz and Band1 from 867.1 MHz to 867.9 MHz).
Table 3: Theoretical Ton-the-air and maximum number of daily packets [10].

## Slide 56: Maximum throughput per end-device and per channel
We can obtain the maximum number of end-devices N.
Scenario 1: maximizing the packets send by the end-devices and throughput of network.
We can obtain the maximum number of end-devices in two different Scenario:
Scenario 2: considering 1 packet per end-device and per day.

## Slide 57: Maximum throughput per end-device and per channel Scenario 1
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0.201625
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0.201625
N
198
N
198
Table 4: Theoretical Ton-the-air and maximum number of daily packets [10].

## Slide 58: Maximum throughput per end-device and per channel Scenario 1
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 1 | 0,066 | 0.00000144
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1 | 1,613 | 0.00000144
N
214149
N
214149
Table 5: Theoretical Ton-the-air and maximum number of daily packets [10].

## Slide 59: Maximum throughput per end-device and per channel
Figure 7: Maximum throughput per end-device and per channel [10].

## Slide 60: We will continue
3- Energy consumption Analyze
1- Delay Analyze
2- Interference Analyze
4- Network model
Channel
Network components
Applications
System model
6- Deep Analyze related work

## Slide 61: Simulation set up
Simulation core
Students of this lab
Other lab students
Students from other laboratories around the world
Industrial companies

## Slide 62: Simulation set up
Deep recognition of the LoRa network
Design flowchart of the algorithms
Write Pseudo code
Architecture and module Design
Technical team
…….
…….
…….
…….
……
…….
Analysis, marketing, management team

## Slide 63: Simulation set up
Platform discrete time simulation
Network simulation is a technique whereby a software program models the behavior of a network by calculating the interaction between the different network entities.
Discrete model: the state variables change only at a countable number of points in time. These points in time are the ones at which the event occurs/change in state.
Network Model
State
Clock
Events list
Random-number generators

## Slide 64: Platform discrete time simulation
NS-3
OMNET++
SimPy
The goal of the ns-3 project is to develop a free and open source simulation environment suitable for networking research. C++ (core) and Python (bindings).
The OMNeT++ simulation kernel is standard C++, and runs basically on all platforms where a modern C++ compiler is available. The Simulation IDE requires Windows, Linux, or macOS.
SimPy is a process-based discrete-event simulation framework based on standard Python. Its event dispatcher is based on Python's generators .

## Slide 65: Reference
[1] Peter J. Ryan 1 and Richard B. Watson, “Research Challenges for the Internet of Things: What Role Can OR Play?” , systems journal, 14 March 2017.
[2] P.P.Ray, A survey on Internet of Things architectures, Journal of King Saud University - Computer and Information Sciences, Volume 30, Issue 3, July 2018, Pages 291-319.
[3] LPWAN white paper, Leverege LLC, 2020 | www.leverege.com
[4] J. Babaki, M. Rasti and R. Aslani, "Dynamic Spreading Factor and Power Allocation of LoRa Networks for Dense IoT Deployments," 2020 IEEE 31st Annual International Symposium on Personal, Indoor and Mobile Radio Communications, 2020, pp. 1-6, doi: 10.1109/PIMRC48278.2020.9217283.
[5] What is LoRaWAN® Specification, https://lora-alliance.org/about-lorawan/

## Slide 66: Reference
[6] V. Talla, M. Hessar, B. Kellogg, A. Najafi, J. R. Smith, S. Gollakota, “LoRa Backscaer: Enabling The Vision of Ubiquitous Connectivity”, Proceedings of the ACM on Interactive, Mobile, Wearable and Ubiquitous Technologies, 2017/9/11.
[7] LoRa™ Modulation Basics, SEMTECH.
[8] Link Budget Calculation, Training materials for wireless trainers, ICTP.
[9] T. Bouguera, J.F. Diouris , J.J Chaillout, R.Jaouadi, G. Andrieux, “Energy Consumption Model for Sensor Nodes Based on LoRa and LoRaWAN”, sensors, 30 June 2018.
[10] E. Ruano, LoRaTM protocol Evaluations, limitations and practical test, May 11, 2016
[11] WIRELESS NETWORKING IN THE DEVELOPING WORLD, http://wndw.net

## Slide 67
THANKS!
You can find me at:
Email: jaber.babaki@gmail.com
GitHub: https://github.com/JaberBabaki
Linkedin: https://www.linkedin.com/in/jaber-babaki-9b5474102/
Telegram: @jaberALU