## Slide 1: Technical overview LoRaWAN network Professor: Dr.Mehdi Rasti Lecturer: Jaber Babaki Amirkabir University of Technology Spring 2021

## Slide 2: HELLO!
I AM JABER BABAKI
You can find me at:
Email: jaber.babaki@gmail.com
GitHub: https://github.com/JaberBabaki
Linkedin: https://www.linkedin.com/in/jaber-babaki-9b5474102/
Telegram: @jaberALU

## Slide 3: BIG CONCEPT
Let’s start with big concept about "Internet of Thing" and "Long Range Wide Area Network"
1

## Slide 4: Introduction
The Internet of Things (IoT) is an extension of the Internet in which large numbers of “things”, including sensors, actuators and processors, in addition to human users, are networked and able to provide high resolution data on their environment and exercise a degree of control over it.
The principal advantage of IoT consists of its ability to enable communication between an infinite amount of machines incorporated into a large-scale wireless network.
These automated devices and sensors together produce and transmit information in real-time, which is useless in the case of incorrect or insuffcient filtering and data processing.

## Slide 5: Introduction
IoT Edge Device
IoT Sensor
Bulk Device Provisioning
etc.,
Cloud Server
IoT Gateway/
Framework
Stream Processing
Things
Insights
Action
User
Management
User
Interface
Machine
Learning
Reporting
Tools
Data Transformation

## Slide 6: Introduction
Many of these are technical, including interoperability and scalability
How to invest in the IoT is a challenge for business
Major social, legal and ethical challenges, including security and privacy
As the future IoT will be a multi-national, multi-industry, multi-technology infrastructure

## Slide 7: The main IoT technical research challenges
Design
Architecture
Interoperability
Scalability
Mobility
Security and Privacy
Scientific/Engineering
Energy efficiency/ Power
Reliability /Robustness
Management/ Operation
Software
Development
Availability
Data management
Cloud computing

## Slide 8: Operation research (OP)
Operation research (OP): the field of OP is an applied discipline which aims to help solve real. It includes many mathematical tools and techniques
OR can support the design management and use of Internet of thing (IoT) which type of new technology which promise to change the world.

## Slide 9: Operation research (OP)
Data Analytic/Database: Data Analytics is the science of studying data to draw conclusions. With billions or even trillions of device connected to the IoT, There will be vast amounts of data including identification, positional, environmental, historical, and descriptive data.
Game theory: Is a method of understanding interactions among groups in conflict with each other. Each side can choose between several actions with the outcome dependent on the actions taken by all players.

## Slide 10: Operation research (OP)
Simulation: Discrete-event simulation simulates the operation of a system as a discrete sequence of events with each event marking a change of state of the system. Between events, no change in the system state is assumed. Discrete-event simulation can be applied to the study of issues in IoT networks.
Fuzzy Systems Theory: Fuzzy systems use fuzzy logic where input variables can take on continuous values, in contrast to digital systems that operate on discrete values. Fuzzy information algorithm using multi-criteria decision analysis and applied it to spacecraft landing safety.

## Slide 11: Operation research (OP)
Artificial Intelligence: The applications of artificial intelligence (AI) and machine learning (ML) technologies in wireless communications have drawn significant attention recently. AI techniques have become an enabler in wireless communications to fulfill the increasing and diverse requirements across a large range of application scenarios.
Queuing Theory: Queuing theory is the mathematical study of queues.. Queuing Theory is an ideal tool for studying behavior of computer networks where the messages (packets) are the customers and the service is the assignment of the messages to communication links [61]. Queuing Theory can help determine network response and throughput by making assumptions about message distribution and node response.

## Slide 12: Operation research (OP)
Graph Theory: Graph theory uses geometric structures (graphs) to model relations between objects. It was invented in the 1700s to solve the Konigsberg Bridge Problem by the famous Swiss mathematician Leonard Euler [63].
Optimization approaches: mathematical programming is the selection of a best element (with regard to some criterion) from some set of available alternatives. Optimization problems of sorts arise in all quantitative disciplines from computer science and engineering to operations research, and the development of solution methods has been of interest in mathematics for centuries

## Slide 13: Communication and transport technologies
An essential requirement for implementing a large and cooperating network of devices is the ability to have a flexible, inexpensive and adaptive connectivity layer.
For these reasons, during the years, several wireless connectivity standards have emerged, ranging from very short-range, low power connections to long-range connectivity solutions based on cellular technologies.
While short-range protocols can be successfully used for a number of applications (e.g., smart homes, wearable, etc.), for many other applications larger coverage radii become mandatory.

## Slide 14: Communication and transport technologies
We expect that in 2024 more than the 40% of the wide area M2M connections will be LPWAN. That is why several companies are developing different protocols to implement the LPWAN technology.

## Slide 15: Communication and transport technologies
To compare the protocols we keep in mind some of the most important characteristics of the LPWAN and some others important features like:
Range: We all know that the range of any wireless technology can vary based on what is in the way of the signal. A dense urban setting, with walls, buildings, reflections, lots of other people and traffic, means much shorter range than a rural one. And a at, unobstructed rural setting will behave better than a hilly one.
Band and spectrum: As we have explained there are protocols that use the free ISM band and others that use licensed spectrum. We can see also differences into the spectrum use, there are some protocols that use Ultra Narrow Band, some are Narrow Band, and some others like LoRa uses Spread Spectrum (Chirp Spread Spectrum).

## Slide 16: Communication and transport technologies
Data Rate: This is another highly variable parameter, it can depend on the distance to the receptor, the obstructions...
Over-the-air updates: This may sound like a random characteristic, but it can be important depending on the application and the deployment of the end-devices. When the number of end-devices is hight or the devices are placed on a remote place, we will get greats advantages of this feature.
Handover: IoT has an extensive application fields, we will find applications where the end-devices will be static units, in other cases they will be mobile (vehicles in urban or rural areas, for farm implementations for example). So it is natural to wonder whether a protocol that can handle the hand-off a device as it moves between hubs, this matters only to the extent that a "session" of some sort is being maintained.

## Slide 17: Communication and transport technologies
 | LoRa | SIGFOX | Telensa | ingenu
Range [km] | 3-8 urban 15-20 suburban | 3-10 urban 30-50 suburban | Up to 8 | 4
Band | Sub-GHz | Sub-GHz | Sub-GHz | 2.4 GHz
Modulation | Spread Spectrum | Ultra-Narrow Band | Ultra-Narrow Band | Spread Spectrum
Data Rate [kbps] | 0.3-22 | 0.1-0.6 | low | 20
OTA upgrades | Yes | No | Yes | Yes
Handover | No | Yes | Yes | Yes

## Slide 18: LoRaWAN network
The LoRaWAN network is formed by two core components: LoRa and LoRaWAN, each of which refers to a layer in the protocol stack. LoRa is a physical layer modulation developed by Semtech. LoRaWAN is implemented on top of the LoRa and includes data link and network layers.
-----
AS 430[MHz]
US 915 [MHz]
EU 433 [MHz]
EU 868 [MHz]
Regional ISM band
LoRa Modulation
Class A
Class B
Class C
MAC options
LoRa MAC
Application
PHY layer (LoRa)
MAC layer (LoRaWAN)
Application layer

## Slide 19: LoRaWAN network
As seen in this figure, the nodes send data to the platform through the gateways. Note that the nodes are not assigned to a specific gateway. Rather, all the gateways in the transmission range of a node receive its data and send it to the platform.
4G/Ethernet/WiFi
G1
G2
G3
Network Server
Application Server

## Slide 20: LoRaWAN network
Processor
Processor
The gateways are connected to the network server via standard IP connections and act as a transparent bridge, simply converting RF packets to IP packets and vice versa.
PHY
SPI
HAL
LoRaWAN Master
Customer Application
BackhaulIP Stack
LoRaWAN Master
Customer Server
Gateway host
PHY
SPI
HAL
Packet Forward
BackhaulIP Stack
Encrypted
Encrypted
Network Server
LoRa FSK
Ethernet, 4G, WiFi

## Slide 21: CSS as a modulation for Long Range
2

## Slide 22: Technical overview CSS as a modulation for Long Range Communication
Long range low power is a family of technologies promising to connect thousands of sensors to the future internet of things. Within this family of possible technology choices, two different branches have emerged
Spread wideband communication
Narrowband communication

## Slide 23: Technical overview CSS as a modulation for Long Range Communication
Frequency
Power
Noise
Narrowband
Spread spectrum
Band of signals occupy a narrow/wide range of frequencies
Power density is high/very low(max power SigFox and LoRa equal 20dBm).
Frequency-hopping spread spectrum (FHSS)
Direct-sequence spread spectrum (DSSS)
Time-hopping spread spectrum (THSS)
Chirp spread spectrum (CSS)

## Slide 24: Technical overview CSS as a modulation for Long Range Communication
Channel Encoder
Input Message
Modulator
Spreading Generator
System
T
F

## Slide 25: Technical overview CSS as a modulation for Long Range Communication
fc
t

## Slide 26: Technical overview CSS as a modulation for Long Range Communication
fc
t
The spreading factor, SF , is the number of bits encoded in each chirp duration.
1
f0
f1
f2
f3
f4
f
f

## Slide 27: Technical overview CSS as a modulation for Long Range Communication
t
t
t
f

## Slide 28: Factors determine RF range
3

## Slide 29: What factors determine RF range and performance?
Link budget : The link budget is the difference between the strength of the transmitted signal and the minimum required signal at the receiver
Transmitter
Receiver

## Slide 30: What factors determine RF range and performance?
Tx radio
cable
ANT
Rx radio
cable
ANT
Path loss

## Slide 31: What factors determine RF range and performance?
Receiving sensitivity: refers to the smallest modulated signal that can be demodulated at the receiving end.
Thermal noise for a 1 Hz bandwidth
Noise figure
Tx power = 14 dBm
BW = 125KHz = 10log10(125000) = 51
NF = 6 dBm
SNR = -20 dBm(for SF=12)
Rx sensitivity = - 174 + 51 + 6 - 20 = -137 dBm
Link budget = -137dB - 14dB = -151dB
Frequency
Power
Noise
LoRa
SNR is key measure in wireless network.
In LoRa network SNR include Noise, SF, BW, TP, CR, Interference

## Slide 32: What factors determine RF range and performance?
Signal-to-Noise Ratio (SNR) : is the ratio between the received power signal and the noise floor power level.

## Slide 33: What factors determine RF range and performance?
:
Typical values ​​of SNR of LoRa are: -20dB and +10dB.
LoRa can demodulate signals below -7.5dB ~ -20dB below the floor noRise.

## Slide 34: Maximum daily packets on LoRaWAN
Duration of the packet transmission
 | Description
SF | Spreading Factor
PL | Payload Length
CRC | The use of the Cyclic Redundancy Check (CRC, 1 when enabled 0 when not)
IH | The use of explicit header or not (IH, 1 when enabled 0 when not)
CR | Coding Rate
DE | The Low Data Rate Optimization (DE, 1 when used 0 when not).

## Slide 35: Maximum daily packets on LoRaWAN
The time that the LoRa Mote has to wait before send the next packet is called Toff
So we can calculate the maximum daily packets

## Slide 36: Maximum daily packets on LoRaWAN
 | 16B | 32B | 51B
7 | 60ms | 90ms | 110ms
8 |  |  | 
9 |  |  | 
10 |  |  | 
11 |  |  | 
12 | 161ms | 213ms | 276ms
 | 16B | 32B | 51B
7 | 13061 | 9657 | 7394
8 |  |  | 
9 |  |  | 
10 |  |  | 
11 |  |  | 
12 | 540 | 408 | 316
we can calculate theoretical Ton-the-air and maximum number of daily packets with variable payload, 8 symbols of preamble, CRC activated with a value of 4/5, Implicit Header deactivated, bandwidth of 125 kHz and Low Data Rate optimization activated for high spreading factors (SF11 and SF12).

## Slide 37: What factors determine RF range and performance?
SF | 125 (kHz) |  |  | 250 (kHz) |  |  | 500 (kHz) |  |  | SNR (dBm) | Range (Km)
 | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) | Bit rate (kb/s) | Sensitivity (dBm) | ToA (ms) |  | 
7 | 5.4 | -124 | 56 | 110 | -122 | 20 | 219 | -116 | 10 | -7.5 | 2
8 |  |  |  |  |  |  |  |  |  |  | 
9 |  |  |  |  |  |  |  |  |  |  | 
10 |  |  |  |  |  |  |  |  |  |  | 
11 |  |  |  |  |  |  |  |  |  |  | 
12 | 0.29 | -137 | 1483 | 0.5 | -135 | 495 | 0.98 | -129 | 247 | -20 | 15
Code rate: 4/5 Payload:10 byte
انجام شبیه سازی با پایتون و پر کردن جدول و کشیدن نمدار بر حسب سایز پکت ارسالی

## Slide 38: ALOHA protocol
4

## Slide 39: ALOHA protocol
Channel Encoder
Input Message
Modulator
Spreading Generator
System
T
F
Channel
Designated frequency
Output signal
Designated frequency
Output signal
Channel
Output signal
Channel
.
.
Designated frequency

## Slide 40: ALOHA protocol
TDMA creates channels by assigning users nonoverlapping time slots. In a system with N users, each user can thus use the total bandwidth W, but only a fraction 1/N of the time
1
2
3
4
T
1
2
3
4
5
6
7
8
9
10
11
12

## Slide 41: ALOHA protocol
Node transmits as soon as it has a frame.
If a collision is detected, it waits for a random time interval and then retransmits.
1
2
3
4
T

## Slide 42: ALOHA protocol
Node transmits as soon as it has a frame.
If a collision is detected, it waits for a random time interval and then retransmits.
Channel
PHY
MAC
New packets
Old packets
packets generation rate per end-devices per time
packets rate send per end-devices per time on channel
Collision?
Average packets generation rate per end-devices per time
Average packets send per end-devices per time on channel

## Slide 43: ALOHA protocol implemented on LoRaWAN

## Slide 44: ALOHA protocol

## Slide 45: Slotted-ALOHA protocol
1
2
3
4

## Slide 46: Slotted-ALOHA

## Slide 47: ALOHA protocol implemented on LoRaWAN
4

## Slide 48: ALOHA protocol implemented on LoRaWAN
λ represents all the packets sent to the network by all the LoRa devices in the same coverage area, so we can rewrite λ as:
Each packet sent by one LoRa device, will select randomly one channel from the 8 available, so the total throughput sent by one LoRa devices per channel will be:

## Slide 49: Maximum throughput per end-device and per channel
 | Max. daily packets per end-device [packets/day] | Max. λi per end-device [packets/sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 0,037
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0,001
Considering packets of 16B payload, a bandwidth of 125 kHz and two available sub-bands on LoRaWAN (Band0 from 868.1 MHz to 868.5 MHz and Band1 from 867.1 MHz to 867.9 MHz).

## Slide 50: Maximum throughput per end-device and per channel
We can obtain the maximum number of end-devices N.
Scenario 1: maximizing the packets send by the end-devices and throughput of network.
We can obtain the maximum number of end-devices in two different Scenario:
Scenario 2: considering 1 packet per end-device and per day.

## Slide 51: Maximum throughput per end-device and per channel Scenario 1
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0.201625
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 26122 | 0,302 | 
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1080 | 0,012 | 0.201625
N
198
N
198

## Slide 52: Maximum throughput per end-device and per channel Scenario 1
 | Max. daily packets per end-device [packets/day] | Ton-the-air [sec] | Max. λ i per channel [packets/sec]
SF7 | 1 | 0,066 | 0.00000144
SF8 |  |  | 
SF9 |  |  | 
SF10 |  |  | 
SF11 |  |  | 
SF12 | 1 | 1,613 | 0.00000144
N
214149
N
214149

## Slide 53: Maximum throughput per end-device and per channel

## Slide 54: تحلیل تاخیر و تحلیل تداخل ارائه بدم تاثیر توان در نرخ داده

## Slide 55: BIG CONCEPT
Bring the attention of your audience over a key concept using icons or illustrations

## Slide 56: IN TWO OR THREE COLUMNS
Yellow
Is the color of gold, butter and ripe lemons. In the spectrum of visible light, yellow is found between green and orange.
Blue
Is the colour of the clear sky and the deep sea. It is located between violet and green on the optical spectrum.
Red
Is the color of blood, and because of this it has historically been associated with sacrifice, danger and courage.

## Slide 57: A PICTURE IS WORTH A THOUSAND WORDS
A complex idea can be conveyed with just a single still image, namely making it possible to absorb large amounts of data quickly.

## Slide 58: WANT BIG IMPACT? USE BIG IMAGE.

## Slide 59: USE DIAGRAMS TO EXPLAIN YOUR IDEAS
Vestibulum nec congue tempus
01
Lorem ipsum dolor
02
Lorem ipsum dolor
03
Lorem ipsum dolor
04
Lorem ipsum dolor
05
Lorem ipsum dolor

## Slide 60: AND TABLES TO COMPARE DATA
 | A | B | C
Yellow | 10 | 20 | 7
Blue | 30 | 15 | 10
Orange | 5 | 24 | 16

## Slide 61: MAPS
our office
Find more maps at slidescarnival.com/extra-free-resources-icons-and-maps

## Slide 62: 89,526,124
Whoa! That’s a big number, aren’t you proud?

## Slide 63: 89,526,124$ 100% 185,244 users
That’s a lot of money
Total success!
And a lot of users

## Slide 64: OUR PROCESS IS EASY
Lorem 3
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Duis sit amet odio vel purus bibendum luctus. Morbi iaculis dapibus tristique. In hac habitasse platea dictumst. Mauris convallis quam at. Morbi iaculis dapibus tristique.
Lorem 1
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Duis sit amet odio vel purus bibendum luctus. Morbi iaculis dapibus tristique. In hac habitasse platea dictumst. Mauris convallis quam at. Morbi iaculis dapibus tristique.
Lorem 2
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Duis sit amet odio vel purus bibendum luctus. Morbi iaculis dapibus tristique. In hac habitasse platea dictumst. Mauris convallis quam at. Morbi iaculis dapibus tristique.

## Slide 65: LET’S REVIEW SOME CONCEPTS
Yellow
Is the color of gold, butter and ripe lemons. In the spectrum of visible light, yellow is found between green and orange.
Blue
Is the colour of the clear sky and the deep sea. It is located between violet and green on the optical spectrum.
Red
Is the color of blood, and because of this it has historically been associated with sacrifice, danger and courage.
Yellow
Is the color of gold, butter and ripe lemons. In the spectrum of visible light, yellow is found between green and orange.
Blue
Is the colour of the clear sky and the deep sea. It is located between violet and green on the optical spectrum.
Red
Is the color of blood, and because of this it has historically been associated with sacrifice, danger and courage.

## Slide 66
You can insert graphs from Excel or Google Sheets

## Slide 67
You can insert graphs from Excel or Google Sheets

## Slide 68
MOBILE PROJECT
Show and explain your web, app or software projects using these gadget templates.
Place your screenshot here

## Slide 69
Place your screenshot here
TABLET PROJECT
Show and explain your web, app or software projects using these gadget templates.

## Slide 70
Place your screenshot here
DESKTOP PROJECT
Show and explain your web, app or software projects using these gadget templates.

## Slide 71: THANKS!
ANY QUESTIONS?
You can find me at:
@username
user@mail.me

## Slide 72: CREDITS
Special thanks to all the people who made and released these awesome resources for free:
Presentation template by SlidesCarnival
Photographs by Unsplash

## Slide 73: PRESENTATION DESIGN
This presentation uses the following typographies:
Titles: Saira Semi Condensed
Body copy: Inria Sans
Download for free at: https://www.fontsquirrel.com/fonts/saira https://www.fontsquirrel.com/fonts/inria-sans
You don’t need to keep this slide in your presentation. It’s only here to serve you as a design guide if you need to create new slides or download the fonts to edit the presentation in PowerPoint®

## Slide 74
SlidesCarnival icons are editable shapes. This means that you can:
Resize them without losing quality.
Change fill color and opacity.
Change line color, width and style.
Isn’t that nice? :) Examples:
Find more icons at slidescarnival.com/extra-free-resources-icons-and-maps

## Slide 75: DIAGRAMS AND INFOGRAPHICS

## Slide 76
✋👆👉👍👤👦👧👨👩👪💃🏃💑❤😂😉😋😒😭👶😸🐟🍒🍔💣📌📖🔨🎃🎈🎨🏈🏰🌏🔌🔑 and many more...
😉
You can also use any emoji as an icon! And of course it resizes without losing quality.
How? Follow Google instructions https://twitter.com/googledocs/status/730087240156643328

## Slide 77
Free templates for all your presentation needs
Ready to use, professional and customizable
100% free for personal or commercial use
Blow your audience away with attractive visuals
For PowerPoint and Google Slides